## Slide 1: Sign Language Interpreter Running on Raspberry Pi
Group ViitTomakieli
Kandel Sushila, Lipponen Seppo, Viitala Jussi & Varpula Teemu

## Slide 2: Introduction
Our project aims to develop a system that can detect Finnish sign language alphabets.
Using OpenCV and MediaPipe .
Running on Raspberry Pi.
Using our own image collection to train the recognition model.
Excluding characters from Z-Ö that would require motion.
Few control signs are added to trigger events like write character, space, backspace and clear buffer.

## Slide 3: Project Overview
Recognition is made from live video feed from the Raspberry Pi Camera Module. If sign is recognized, it will be show in text screen for the receiver and signer.
  Hardware Requirements:
    ⦁ Raspberry Pi
    ⦁ Raspberry Pi Camera Module
    ⦁ 1602 LCD display (Optionally can use second one for the signer)
  Software Requirements:
    ⦁ Python
    ⦁ OpenCV
    ⦁ MediaPipe
Notes: Sushila

## Slide 4: Project Version and Deadline
Project Version | Deadline for System Completion | Relevant Dates | Scope and Deliverables
1.0 | 1.3.2024 | 26.2.2024 | Raspberry Pi setup
1.1 | 6.3.2024 | 29.2.2024 | Raspberry Pi image recognition
1.2 | 8.3.2024 | 8.3.2024 | Raspberry Pi working display
1.3 | 8.3.2024 | 8.3.2024 | Three- character identification
1.4 | 15.3.2024 | 15.3.2024 | Whole alphabet identification and control commands
1.5 | 27.3.2024 | 27.3.2024 | Document including implementation
1.6 | 4.4.2024 | 4.4.2024 | Casing the hardware in card box
2.0 | 4.4.2024 | 4.4.2024 | Sign Detector final version

## Slide 5
Notes: Kytkentäkaavio, ja on kaksi näyttö. I2C upper on , and lower one is . Raspberry Pi 4B.
Toinen näyttö I2c piirillä ja toinen ilman

## Slide 6: Images
Notes: kytkentälevy

## Slide 7
Notes: Pätkä ohjelman toiminnasta

## Slide 8: Functional Implementation
Creating model
  Collecting images
    Capturing sign images. We used 100 images per sign
  Create dataset
    Getting hand landmarks from images and saving them for training
  Training model
    Creating recognition model from dataset using random forest classifier

## Slide 9: Functional Implementation
Comparing sign gestures
  Image Capturing
    Capturing image with pi camera
  Getting hand landmarks
    Finding hand from image
    Getting hand landmarks and saving datapoints
  Depending on hand of the regognized sign
    Left is used for commnads
    Right for alphabet signs
  Recognized alphabet can be added or removed from ledscreen

## Slide 10
Sign Detector Flowchart

## Slide 11: Limitations
Missing few characters
  Signs that need movement recognition
    J is made with still image because it differs enough with other signs.
    Z,Å,Ä,Ö signs are not include due to the motion requirement.
    Detection of these left out signs will be left for future versions
Hardware limitations
  Raspberry still needs powercord to operate
  Dataset training still requires external display

## Slide 12: Challenges
Multiple operating systems
Windows, macOs, Linux
Required python versions
First we had different python versions while compiling code
Creating dataset with different devices
Different resolutions of cameras

## Slide 13: Implementation Changes
Changes to original requirements
  External buttons are replaced with hand commands
  Leds are replaced wth LCD and keyboard
  Carboard case replaced 3D printed casing

## Slide 14: Possible Improvements
Refinement of UX
Movement interpreter addition
3D printed case
Replacing breadboard with custom PCB
2 way communication
Bigger screens with more information